## Slide 1: Thermal Model Parameter Identification Algorithm
Greg Fiore
gregfiore@gmail.com
2/10/2012

## Slide 2: Overview
Could the thermal properties of a building and its heating system be determined by a thermostat?
Approach
  Turn heat on for a short period
  Observe response
  Compute thermal parameters based on a simple thermodynamic model
Potential advantages
  New control algorithms
  Reduced overshoot due to latent heating
  Improved “time to temperature” estimates
  Energy consumption predictions

## Slide 3: Model
Simple thermodynamic model with forced-air heating system
Simulink model

## Slide 4: Normal Thermostat Operation
Thermostat keeps house temperature within 4 degrees of set-point despite fluctuation in outside temperature.
Set-point

## Slide 5: Learning Mode Algorithm
Turn on Heater for X mins
Identify windows of thermal response:
Heat on, house warming
Heat off, house cooling
Estimate C1 with data when heater is off and house is cooling
Estimate C2 and Theater data when heat is on using least squares fit of data
House temp.
Outdoor temp.

## Slide 6: Prediction Accuracy
All parameters estimated to within 20% for a broad range of heater temperatures and house heat loss coefficients
Theater and Req estimated to within 6.5% accuracy
With little insulation, less heat retention results in poor estimate

## Slide 7: Conclusions
Accurate estimates of building heat parameters can be made using a learning algorithm
Further work
  Increase model fidelity
  Sensitivity testing
  Develop new algorithms that make use of estimated parameters
  Investigate feasibility of implementation on the Nest device